## Slide 1: ELECTRIC PARKING BRAKE SYSTEMS
doc. Juraj PANČÍK
PRESENTATION WILL BE FOUND AT: www.drpancik.sk
PROFILE: https://www.linkedin.com/in/juraj-pancik-phd-36794a53/?originalSubdomain=sk
KME FEIT UNIZA

## Slide 2: Introduction
Hydraulic brake calipers are a vital part of your vehicle's braking system. Brake calipers squeeze the brake pads against the surface of the brake rotor to slow or stop the vehicle.
Hydraulic brake calipers are essential to your car's ability to stop and are arguably one of the most important automobile brake parts.
Most cars today have disc brakes, at least for the front wheels, anyway. But a lot of cars and trucks are now using disc brakes in the rear, too.
In a disc-braking system the car's wheels are attached to metal discs, or rotors, that spin along with the wheels.
The job of the caliper is to slow the car's wheels by creating friction with the rotors.

## Slide 3: Introduction - Caliper integrated EPB
  Components of the calipers with integrated Electronic Parking Brakes are :
    Hydraulic brake caliper (incl. anchor, springs, bearings)
    Brake disc
    Brake pads
    Motor-Gear-Unit (MGU)
    Electronic Stability Control (ESC) system
    All above components are mentioned in our article as automotive components and we deal with their fatigue tests machines
PHOTO TAKEN FROM : Mr. Christian Quasten; Dr. Gunther Seipel; Mr. Sebastian Fischer Continental AG, Frankfurt, Germany : The influence of brake ad properties on the hill hold performance of a caliper integrated EPB-System at Euro Brake Conference 2016, MILAN, Italy

## Slide 4
Encyclopedia of Automotive Engineering Online ISBN: 9781118354179
Editor(s): Professor David Crolla; Professor David E. Foster; Professor Toshio Kobayashi; Professor Nicholas Vaughan
Wiley, 2017

## Slide 5: Caliper integrated EPB – forecasting
GRAPH TAKEN FROM : Dr. Reitz, Andreas, Loehr, Bert, Kohrt, Jens-PeterZF-TRW Active & Passive Safety Technology, Germany : HARMONISATION OF THE RELEASE PROCESS FOR ELECTRIC PARKING BRAKE SYSTEMS at Euro Brake Conference 2016, MILAN, Italy

## Slide 6: Introduction - Electronic Stability Control (ESC) and EPB
Electronic Stability Control (ESC) is an active safety system that recognizes unstable driving conditions at the very outset and applies automatic and immediate, corrective action, if necessary.
ESC, presently the most important active safety system, prevents critical vehicle states from developing. The system constantly evaluates the data from the wheel speed sensors, the steering angle sensor, the yaw rate and lateral acceleration sensor and compares the driver’s input with the vehicle’s actual behavior. If an unstable state is detected, for instance as the result of a sudden direction change, ESC responds in milliseconds and stabilizes the vehicle through wheel-specific brake intervention and adjustment of the engine torque.
ESC is the sum of the following functions:
  ABS Anti-lock Brake System
  EBD Electronic Brake force Distribution
  TCS Traction Control System
  AYC Active Yaw Control
Source :
http://www.continental-automotive.com/www/automotive_de_en/themes/passenger_cars/chassis_safety/ved/ebs_family_en.html?page=3

## Slide 7: MK100ESC + IPB (integrated parking brake)
Functions
Static Apply and Release
DAR (Drive Away Release)
Dynamic Brake Function via ESC and/or IPB actuator
Hot Disk Re-clamp
Roller dyno detection
Technical Data IPB
Clamping force : up to 18 kN
Apply time: ~1,0s to Fmax
Release time: ~0,8s
Life time: 100.000 cycles with Fmax
IPB
Actuator
Actuator
2x Motor
2x Motor
12V
EPB
Switch
CAN
2x CAN H/L
ESC
Switch
ESC ECU
EPB ECU
MK100 + IPB
Cable length ~7,5m
single way
all known EPB functions available
hydraulic
hydraulic

## Slide 8
IPB – Integrated Parking Brake

## Slide 9: IPB caliper in sectioning

## Slide 10
K. Reif (Ed.), Brakes, Brake Control and Driver Assistance Systems, Bosch Professional
Automotive Information, DOI 10.1007/978-3-658-03978-3_4, © Springer Fachmedien Wiesbaden 2014

## Slide 11
K. Reif (Ed.), Brakes, Brake Control and Driver Assistance Systems, Bosch Professional
Automotive Information, DOI 10.1007/978-3-658-03978-3_4, © Springer Fachmedien Wiesbaden 2014

## Slide 12
Encyclopedia of Automotive Engineering Online ISBN: 9781118354179
Editor(s): Professor David Crolla; Professor David E. Foster; Professor Toshio Kobayashi; Professor Nicholas Vaughan
Wiley, 2017

## Slide 13
Encyclopedia of Automotive Engineering Online ISBN: 9781118354179
Editor(s): Professor David Crolla; Professor David E. Foster; Professor Toshio Kobayashi; Professor Nicholas Vaughan
Wiley, 2017

## Slide 14
K. Reif (Ed.), Brakes, Brake Control and Driver Assistance Systems, Bosch Professional
Automotive Information, DOI 10.1007/978-3-658-03978-3_4, © Springer Fachmedien Wiesbaden 2014

## Slide 15
Encyclopedia of Automotive Engineering Online ISBN: 9781118354179
Editor(s): Professor David Crolla; Professor David E. Foster; Professor Toshio Kobayashi; Professor Nicholas Vaughan
Wiley, 2017

## Slide 16
Encyclopedia of Automotive Engineering Online ISBN: 9781118354179
Editor(s): Professor David Crolla; Professor David E. Foster; Professor Toshio Kobayashi; Professor Nicholas Vaughan
Wiley, 2017

## Slide 17: V-model DEVELOPMENT PHASES

## Slide 18
Encyclopedia of Automotive Engineering Online ISBN: 9781118354179
Editor(s): Professor David Crolla; Professor David E. Foster; Professor Toshio Kobayashi; Professor Nicholas Vaughan
Wiley, 2017

## Slide 19
Anchor
Bleed Screw
Bleeder (or Dust) Cap
Guide Pin
Housing Clip (or Spring)
Outer Pad
Inner Pad
Motor Gear Unit (MGU)
Electrical Connector on MGU
(Not Visible)
Ball Screw Assembly
w/ O-Ring
Piston
Piston Seal
Dust Boot
Electronic Parking Brake (EPB) Nomenclature (1 of 4)

## Slide 20
Housing
Hose Anti -Rotation Hole
Inlet Protection Plug
Protection Plugs
Bushings
Electronic Parking Brake (EPB) Nomenclature (2of 4)

## Slide 21
Electronic Parking Brake (EPB) Nomenclature (3 of 4)
Head Cap Screws
Identification Label
Julian Date Code Area
MGU Data Matrix Code

## Slide 22
Backplate of Outer Pad
Anchor Mounting Threads
Electronic Parking Brake (EPB) Nomenclature (4 of 4)